# (Your Business Name Here) – Safe Work Procedure

# POST HOLE DIGGER – TRACTOR OPERATED

DO NOT use this machine unless you have been instructed

in its safe use and operation and have been given permission

## PERSONAL PROTECTIVE EQUIPMENT

## PRE-OPERATIONAL SAFETY CHECKS

Locate and ensure you are familiar with all machine operations and controls.

Ensure all guards are fitted, secure and functional. Do not operate if guards are missing or faulty.

Check all pins, bolts and connections to ensure all are securely in place.

Ensure the shear bolts or auger-retaining bolts have not been replaced with ones longer than those supplied and specified by the manufacturer.

Do not use the digger unless the auger point and cutting edges are intact and in good working order.

Ensure the posthole digger is attached to the tractor according to the manufacturer’s specification.

## OPERATIONAL SAFETY CHECKS

Reduce speed when transporting mounted implements to avoid bouncing and momentary loss of steering control.

Posthole diggers are designed for one-person operation.

Always dig holes while sitting in the tractor seat.

Ensure no one is near you when you operate the posthole digger.

Ensure the work area is free from underground cables or pipes.

Clear area of stones, branches or other debris that might be thrown or become entangled.

Inspect the entire machine periodically. Look for loose fasteners, worn or broken parts, pinched hydraulic hoses, and leaky or loose fittings.

Do not attempt to free the auger while the PTO is connected. Disconnect the PTO driveline from the tractor before attempting to free the auger. Repair and/or replace as needed.

## ENDING OPERATIONS AND CLEANING UP

Always stop the PTO, set the brake, shut off the tractor engine, remove the tractor key and allow the auger to come to a complete stop before dismounting tractor.

## POTENTIAL HAZARDS AND INJURIES

Rotating parts.

Hair/clothing getting caught in moving machine parts.

Noise.

Flying debris.

## DON’T

Do not use faulty equipment. Report suspect machinery immediately.

Never wear loose clothing, jewellery, or have long hair untied while operating a post hold digger.

Do not operate digger on steep hillsides. When digging on uneven or hilly terrain, position the tractor with the posthole digger uphill.

Do not let the auger screw itself into the ground. The auger must dig with the dirt breaking up and being carried to the top by the auger flutes.

Do not shovel dirt away from a rotating auger as the shovel can be caught and thrown by the auger.

Do not walk or work under a raised digger or attachment unless it is securely blocked or held in position.

Never leave equipment unattended with the tractor running.

This SWP does not necessarily cover all possible hazards associated with this equipment and should be used in conjunction with other references.  It is designed as a guide to be used to compliment training and as a reminder to users prior to equipment use.

This information is based on material published by the South Australian Department of Education and Children’s Services.