# (Your Business Name Here) – Safe Work Procedure

# STATIONARY ENGINE

DO NOT use this machine unless you have been instructed

in its safe use and operation and have been given permission

## PERSONAL PROTECTIVE EQUIPMENT

| Safety glasses must be worn at all times in work areas. | Long and loose hair must be contained. | Hearing protection must be worn. |
| --- | --- | --- |
| Sturdy footwear must be worn at all times in work areas. | Close fitting/protective clothing must be worn. | Rings and jewellery must not be worn. |

## PRE-OPERATIONAL SAFETY CHECKS

Locate and ensure you are familiar with all machine operations and controls.

Ensure all guards are fitted, secure and functional. Do not operate if guards are missing or faulty.

Ensure the engine has operating and maintenance instructions permanently located and clearly visible.

Ensure the area is clean and clear of grease and oil.

Check workspaces and walkways to ensure no slip/trip hazards are present.

Check all safety devices are in good condition.

Ensure the work area is well ventilated. Start the fume extraction unit before using the machine.

Ensure all flammable materials are correctly stored before operating.

## OPERATIONAL SAFETY CHECKS

Only one person shall operate the engine at a time.

Ensure the area is clear of people and equipment before operating.

During operation and when cooling down, be aware that parts of the plant are hot and/or rotating.

## ENDING OPERATIONS AND CLEANING UP

Switch off the machine when work completed.

Ensure the battery (if fitted) and fuel line are turned off.

Keep the equipment and work area in a safe, clean and tidy state.

## POTENTIAL HAZARDS

Hot components.

Hair/clothing getting caught in moving machine parts.

Fume.

Trapping hazards.

Crushing hazards.

Fire.

Fuel.

## DON’T

Do not use faulty equipment. Immediately report suspect equipment.

Never leave the machine running unattended.

This SWP does not necessarily cover all possible hazards associated with this equipment and should be used in conjunction with other references.  It is designed as a guide to be used to compliment training and as a reminder to users prior to equipment use.

This information is based on material published by the South Australian Department of Education and Children’s Services.